B3DM Feature Table Global

Property	Type	Description
BATCH_LENGTH	uint32	The number of distinguishable models (features) in the batch. If the binary glTF does not have a batchId attribute, this field must be 0.
RTC_CENTER	float32[3]	The center position when positions are defined relative-to-center

I3DM Feature Table Global

Property	Type	Description
INSTANCES_LENGTH	uint32	The number of instances
QUANTIZED_VOLUME_OFFSET	float32[3]	The offset of the quantized volume in x, y, and z-direction
QUANTIZED_VOLUME_SCALE	float32[3]	The scale of the quantized volume in x, y, and z-direction
EAST_NORTH_UP	boolean	Whether the instance orientation should default to the east/north/up reference frame on the WGS84 ellipsoid
RTC_CENTER	float32[3]	The center position when positions are defined relative-to-center

I3DM Feature Table Instance

Property	Type	Description
POSITION / POSITION_QUANTIZED	float32[3] / uint16[3]	The x,y, and z coordinates for the position of the instance
NORMAL_UP / NORMAL_UP_OCT32P	float32[3] / uint16[2]	A unit vector defining the up-direction of the instance
NORMAL_RIGHT / NORMAL_RIGHT_OCT32P	float32[3] / uint16[2]	A unit vector defining the right-direction of the instance
SCALE	float32	A scaling factor for all axes of the instance
SCALE_NON_UNIFORM	float32[3]	The scaling factors for the x, y, and z-axis of the instance
BATCH_ID	uint8/16/32	The batch ID, to look up metadata for the instance in the batch table

PNTS Feature Table Global

Property	Type	Description
POINTS_LENGTH	uint32	The number of points
QUANTIZED_VOLUME_OFFSET	float32[3]	The offset of the quantized volume in x, y, and z-direction
QUANTIZED_VOLUME_SCALE	float32[3]	The scale of the quantized volume in x, y, and z-direction
CONSTANT_RBGA	uint8[4]	The RGBA color components for all points in the tile
BATCH_LENGTH	uint32	The number of batches for the points
RTC_CENTER	float32[3]	The center position when positions are defined relative-to-center

PNTS Feature Table Point

Property	Type	Description
POSITION / POSITION_QUANTIZED	float32[3] / uint16[3]	The x,y, and z coordinates for the position of the point
RGBA	uint8[4]	The RGBA color components of the point
RGB	uint8[3]	The RGB color components of the point
RGB565	uint16	A compressed, 16bit representation of RGB colors, with 5 bits for red, 6 bits for green, and 5 bits for blue
NORMAL / NORMAL_OCT16P	float32[3] / uint8[2]	A unit vector defining the normal of the point
BATCH_ID	uint8/16/32	The batch ID, to look up metadata for the points the batch table

componentType	Size in bytes
“BYTE“	1
“UNSIGNED BYTE“	1
“SHORT“	2
“UNSIGNED SHORT“	2
“INT“	4
“UNSIGNED INT“	4
“FLOAT“	4
“DOUBLE“	8

type	Number of components
“SCALAR“	1
“VEC2“	2
“VEC3“	3
“VEC4“	4